# Monitoring gluster/Red Hat Storage with “gtop”
## Background
Monitoring single systems on any operating system is a straight forward task. However, the options available when monitoring performance across a 'cluster' whilst maintaining the context of the service the cluster provides is more problematic.

The glusterfs/vdsm components of Red Hat Storage do not currently expose monitoring information. In order to provide a view of what's going on within the cluster, SNMP is a readily available data source provides most of the data that interests Storage/System Administrators.

Gtop provides a command line tool, that brings together the SNMP statistics within the context of gluster (nodes, volumes, bricks) allowing administrators to see performance and capacity information in one place. In addition to these metrics, gtop also performs checks on the presence of the glusterd process, alerting visually to any node/glusterd disruption.

'Skew' shows the max clock difference across the node samples

Node area showing activity metrics for each node in the cluster / Volume area providing a capacity centric view of the volumes provided by the cluster	Daemons monitored / C … CTDB H … Self Heal / S … Samba G … Georeplication / N … NFS (gNFS)	Cluster area, providing an aggregated view of capacity and performance

Using SNMP as the data source isn't perfect, so it's good to understand the downsides to the way this tool gathers data. The bulk of the data provided by the SNMP agent is only refreshed every 5 seconds, so more granular performance analysis is not possible. In addition, the SNMP agent response can get delayed when nodes approach 70-80% CPU which can result in nodes temporarily dropping to an unknown state.

gtop is a python program, based on python 2.6 for RHEL6+ compatibility
- Python's multiprocessing module is used to place the SNMP data gathering separate processes. Python's SNMP binding are synchronous, so without this approach data gathering can be blocked by a single node. Other projects like 'twisted' could be exploited, but require further dependencies to be resolved – so I've tried to keep the deployment simple to provide a broader compatibility.
- Python supports PIPE's between the processes for data exchange, and shared memory for read only purposes. This means that when gtop starts there are 2 pids to manage the UI and memory, and secondary processes for each node's SNMP data gathering.
- The UI is designed with the constraints of an 80x24 window (local console).
- Resizing the UI window when running under X windows is currently not supported, and results in program termination.
- The screen refreshes every 5 seconds automatically
- Sorting volume and node data areas is supported (see below)
- As well as a UI, the program accepts a server list or group of servers. In this mode, the program displays node statistics only to stdout.

## Installation Steps
### Prerequisites
In order to use the tool, the following packages (RPMS) need to be installed on each gluster/RHS node.
- net-snmp
- net-snmp-utils
- net-snmp-python

SNMP needs to be configured to enable gtop to gather usage metrics. A sample snmpd.conf file is provided which allows local write access, and remote read access to the SNMP MIBs based on a community string of 'gluster'. The community name can be changed either in the code, or by providing a parameter override in the gtoprc.xml file (see appendices)

Although the bulk of the system stats are restricted to a 5 second refresh rate due to the snmp agent, network statistics can be tuned down to 1 second sample rates which improves the accuracy of the UI. It is therefore recommended that the following snmpset command is added to the rc.local file on each node.

snmpset -c <community name> -v2c 127.0.0.1 1.3.6.1.4.1.8072.1.5.3.1.2.1.3.6.1.2.1.2.2 i 1

Once snmpd is installed and the snmpd.conf file is in place, the snmpd daemon needs to be enabled and started.

>chkconfig snmpd –level 3 on
>service snmpd start

It is also recommended that gtop is deployed to each of the nodes, and placed in /root/bin.

## Usage
Gtop initially looks for a configuration file. This file can be used to provide 2 things;
server groups	assigning a single name to a group of servers (used in batch mode)
runtime overrides	changing disk block size, SNMP community string, influencing UI layout ratios (volume vs nodes)

An example of the configuration is provided in the appendices.

The overrides mechanism provides an easy way to change the way the program interacts with SNMP without changing the code itself.

In addition to the UI shown, gtop can also be started in 'batch' mode. This mode accepts a list of servers or a group name and simply writes node usage statistics to stdout every 5 seconds.
e.g.
[root@rhs5-1 ~]# gtop -g rhs5

gtop starting
Applying overrides from configuration file
SNMPCOMMUNITY = 'RHS'
BLOCKSIZE = 512
VOLUMEAREAPCT = 30
NODEAREAPCT = 50
Checking supplied server list is usable..
Checking SNMP is available on the selected hosts..
---> rhs5-1 OK
---> rhs5-2 OK
        CPU Memory % Network AVG Disk I/O AVG
  Time Gluster Node C/T % RAM Real Swap In Out Reads Writes
-------- --------------- --- --- ----- ----|---- ------|------ ------|------
16:47:19 rhs5-1 2 0 491M 92 0 0b 0b 0b 0b
16:47:19 rhs5-2 2 0 491M 93 0 0b 0b 0b 0b
16:47:24 rhs5-1 2 3 491M 92 0 4K 4K 245K 0b
16:47:24 rhs5-2 2 0 491M 93 0 4K 3K 0b 0b
16:47:29 rhs5-1 2 3 491M 92 0 5K 5K 0b 12K
16:47:29 rhs5-2 2 2 491M 93 0 5K 4K 0b 3K
16:47:34 rhs5-1 2 1 491M 92 0 4K 4K 0b 4K
16:47:34 rhs5-2 2 0 491M 93 0 4K 3K 0b 6K
16:47:39 rhs5-1 2 1 491M 92 0 4K 4K 0b 0b
16:47:39 rhs5-2 2 0 491M 93 0 4K 3K 0b 512b
^CProgram terminated.
[root@rhs5-1 ~]#

Using gtop via the UI provides a means of observing the performance and capacity utilisation in the cluster, in near real-time. The console provides a means of sorting the data displayed, allowing both forward and reverse sorts to be performed.

The sort keys work as toggles providing sort direction changes.

Window Area	Keys	Sort Sequence
Volume Information	F/f	Freespace
	V/v	Volume name
	S/s	Volume Size

Window Area	Keys	Sort Sequence
Node Information	N/n	Node name
	C/c	CPU Busy
	I/i	Network in rate
	O/o	Network Out rate
	R/r	Disk Read average
	W/w	Disk Write average

The volume and node area are also scrollable allowing for larger cluster configurations. The volume area highlight bar moves using the up/down cursor keys. The node area uses + and – keys to move the node list up and down.

Individual node statistics are aggregated at each interval and displayed in the info area at the top of the UI. This area provides an insight into the workload running against the entire cluster. As well as the node metrics, each sample interval also brings the nodes timestamp, enabling a time skew to be calculated across the nodes. A skew of <5s is OK, since this is the sample interval – but larger skew times may indicate inconsistent ntpd configurations which would make geo-replication transfers inconsistent.

In addition to the performance and capacity metrics, gtop also checks for the presence specific daemons on each node. Initially this was just glusterd, but now the process monitoring checks for the presence of the following;
- ctdb
- samba
- nfs
- self heal
- geo-replication

Each node listed in the UI has a status icon* in the first column, which changes based on the status of glusterd and SNMP on that node

	Glusterd process on the node is present, and SNMP is responding
	Glusterd process was not found in the current process list, and SNMP is responding
?	SNMP for the node is not responding – node could be down, or SNMP community may be incorrect

* the icons used varies between console tty access and xterm. The icons shown above are those used within an x windows environment.

## Feedback
 For further information, enhancement ideas or code contributions please contact

paul dot cuzner at gmail dot com

## Known Issues
1. The console UI uses unicode characters to indicate the state of the node. On some tty's these codes do not render properly.
2. If the network cache timeout snmp setting is not set to 1, every other sample interval will return a high value for the network in/out stats.
3. When Nodes become busy, or the network congested, SNMP responses will be effected which gtop will respond to by indicating '?' against the node.
## Appendices

### gtoprc.xml
<gtop>
<parameters>
<SNMPCOMMUNITY="gluster"/>
<BLOCKSIZE=512/>
<VOLUMEAREAPCT=.3/>
<NODEAREAPCT=.5/>
</parameters>
<grouplist>
<group name="services">
<server name="svcs"/>
</group>
<group name="rhs1">
<server name="rhs-1"/>
<server name="rhs-2"/>
<server name="rhs-3"/>
<server name="rhs-4"/>
</group>
<group name="rhs5">
<server name="rhs5-1"/>
<server name="rhs5-2"/>
</group>
</grouplist>
</gtop>