# Monitoring gluster/Red Hat Storage with “gtop”
## Background
Monitoring single systems on any operating system is a straight forward task. However, the options available when monitoring performance across a 'cluster' whilst maintaining the context of the service the cluster provides is more problematic.

The glusterfs/vdsm components of Red Hat Storage do not currently expose monitoring information. In order to provide a view of what's going on within the cluster, SNMP is a readily available data source provides most of the data that interests Storage/System Administrators.

Gtop provides a command line tool, that brings together the SNMP statistics within the context of gluster (nodes, volumes, bricks) allowing administrators to see performance and capacity information in one place. In addition to these metrics, gtop also performs checks on the presence of the glusterd process, alerting visually to any node/glusterd disruption.

Cluster information, provided an aggregated view of capacity and performance

Volume area providing a capacity centric view of the volumes provided by the cluster	gtop - 3.3.0.5rhs 2 nodes, 2 active CPU%: 2 Avg, 2 peak 10:44:42 / Activity - Network: 12K in, 12K out Disk: 0b reads, 0b writes / Storage - 3 volumes, 6 bricks / 5G raw, 2G usable, 253M used, 2G free / Volume Bricks Type Size Used Free Volume Usage / ctdb 2 R 491M 25M 466M █ 5% / ftp 2 R 991M 33M 959M █ 3% / repl 2 R 1015M 195M 820M ███ 19% / CPU Memory % Network AVG Disk I/O AVG / S Gluster Node C/T % RAM Real|Swap In | Out Reads | Writes / ▲ rhs5-1 2 2 491M 92 0 5K 5K 0b 0b / ▲ rhs5-2 2 2 491M 88 0 7K 7K 0b 0b / Node area showing activity metrics for each node in the cluster

Using SNMP as the data source isn't perfect, so it's good to understand the downsides to the way this tool gathers data. The bulk of the data provided by the SNMP agent is only refreshed every 5 seconds, so more granular performance analysis is not possible. In addition, the SNMP agent response can get delayed when nodes approach 70-80% CPU which can result in nodes temporarily dropping to an unknown state.

The gtop program is based on python (2.6, for RHEL6+ compatibility).
- Python's multiprocessing module is used to place the SNMP data gathering separate processes. Python's SNMP binding are synchronous, so without this approach data gathering can be blocked by a single node.
- Python supports PIPE's between the processes for data exchange, and shared memory for read only purposes. This means that when gtop starts there are 2 pids to manage the UI and memory, and secondary processes for each node's SNMP data gathering.
- The UI is designed with the constraints of an 80x24 window (local console).
- Resizing the UI window when running under X windows is currently not supported, and results in program termination.
- The screen refreshes every 5 seconds automatically
- Sorting volume and node data areas is supported (see below)
- As well as a UI, the program accepts a server list or group of servers. In this mode, the program displays node statistics only to stdout.

## Installation Steps
### Prerequisites
In order to use the tool, the following packages (RPMS) need to be installed on each gluster/RHS node.
- net-snmp
- net-snmp-utils
- net-snmp-python

SNMP needs to be configured to enable gtop to gather usage metrics. A sample snmpd.conf file is provided which allows local write access, and remote read access to the SNMP MIBs based on a community string of 'gluster'. The community name can be changed either in the code, or by providing a parameter override in the gtoprc.xml file (see appendices)

Although the bulk of the system stats are restricted to a 5 second refresh rate due to the snmp agent, network statistics can be tuned down to 1 second sample rates which improves the accuracy of the UI. It is therefore recommended that the following snmpset command is added to the rc.local file on each node.

/sbin/snmpset -c <community name> -v2c 127.0.0.1 1.3.6.1.4.1.8072.1.5.3.1.2.1.3.6.1.2.1.2.2 i 1

Once snmpd is installed and the snmpd.conf file is in place, the snmpd daemon needs to be enabled

>chkconfig snmpd –level 3 on
>service snmpd start

It is also recommended that gtop is deployed to each of the nodes, and placed in /root/bin.

## Usage
Gtop initially looks for a configuration file. This file can be used to provide 2 things;
server groups	assigning a single name to a group of servers (used in batch mode)
runtime overrides	changing disk block size, SNMP community string, influencing UI layout ratios (volume vs nodes)

An example of the configuration is provided in the appendices.

The overrides mechanism provides an easy way to change the way the program interacts with SNMP without changing the code itself.

In addition to the UI shown, gtop can also be started in 'batch' mode. This mode accepts a list of servers or a group name and simply writes node usage statistics to stdout every 5 seconds.
e.g.
[root@rhs5-1 ~]# gtop -g rhs5

gtop starting
Applying overrides from configuration file
SNMPCOMMUNITY = 'RHS'
BLOCKSIZE = 512
VOLUMEAREAPCT = 30
NODEAREAPCT = 50
Checking supplied server list is usable..
Checking SNMP is available on the selected hosts..
---> rhs5-1 OK
---> rhs5-2 OK
        CPU Memory % Network AVG Disk I/O AVG
  Time Gluster Node C/T % RAM Real Swap In Out Reads Writes
-------- --------------- --- --- ----- ----|---- ------|------ ------|------
16:47:19 rhs5-1 2 0 491M 92 0 0b 0b 0b 0b
16:47:19 rhs5-2 2 0 491M 93 0 0b 0b 0b 0b
16:47:24 rhs5-1 2 3 491M 92 0 4K 4K 245K 0b
16:47:24 rhs5-2 2 0 491M 93 0 4K 3K 0b 0b
16:47:29 rhs5-1 2 3 491M 92 0 5K 5K 0b 12K
16:47:29 rhs5-2 2 2 491M 93 0 5K 4K 0b 3K
16:47:34 rhs5-1 2 1 491M 92 0 4K 4K 0b 4K
16:47:34 rhs5-2 2 0 491M 93 0 4K 3K 0b 6K
16:47:39 rhs5-1 2 1 491M 92 0 4K 4K 0b 0b
16:47:39 rhs5-2 2 0 491M 93 0 4K 3K 0b 512b
^CProgram terminated.
[root@rhs5-1 ~]#

Using gtop via the UI provides a means of observing the performance and capacity utilisation in the cluster, in near real-time. The console provides a means of sorting the data displayed, allowing both forward and reverse sorts to be performed.
The sort keys work as toggles providing sort direction changes.

Window Area	Keys	Sort Sequence
Volume Information	F/f	Freespace
	V/v	Volume name
	S/s	Volume Size

Window Area	Keys	Sort Sequence
Node Information	N/n	Node name
	C/c	CPU Busy
	I/i	Network in rate
	O/o	Network Out rate
	R/r	Disk Read average
	W/w	Disk Write average

The volume area is also scrollable using the up and down arrows, enabling configurations with larger volume counts to be monitored.

Individual node statistics are aggregated at each interval and displayed in the info area at the top of the UI. This area provides an insight into the workload running against the entire cluster.

In addition to the performance and capacity metrics, gtop also checks for the presence of glusterd on each of the nodes. Each node shown has a status indicator in the first column, which changes based on the status of glusterd and SNMP on that node

	Glusterd process on the node is present, and SNMP is responding
	Glusterd process was not found in the current process list, and SNMP is responding
?	SNMP for the node is not responding – node could be down, or SNMP community may be incorrect

## Feedback
 For further information, enhancement ideas or code contributions please contact

paul.cuzner@redhat.com

## Known Issues
The console UI uses unicode characters to indicate the state of the node. On some tty's these codes do not render properly.
## Appendices

### gtoprc.xml
<gtop>
<parameters>
<SNMPCOMMUNITY="gluster"/>
<BLOCKSIZE=512/>
<VOLUMEAREAPCT=.3/>
<NODEAREAPCT=.5/>
</parameters>
<grouplist>
<group name="services">
<server name="svcs"/>
</group>
<group name="rhs1">
<server name="rhs-1"/>
<server name="rhs-2"/>
<server name="rhs-3"/>
<server name="rhs-4"/>
</group>
<group name="rhs5">
<server name="rhs5-1"/>
<server name="rhs5-2"/>
</group>
</grouplist>
</gtop>